## Slide 1: Roadway Development Operators’ Workshop ACARP project C18023 CM2010 – Continuous Miner automation
Dr David Hainsworth
Dr David C. Reid
3-6 March, 2009
Notes: <number>

## Slide 2: CM automation project goals
Key objectives
  Develop CM navigation and localisation systems to deliver remotely supervised, self-steering capability
  Provide real-time machine position and operational info to support autonomous bolting, meshing and haulage systems.
Notes: <number>

## Slide 3: Project at a glance
Full project is 3 years
Present ACARP project 18 months (started Feb 09)
Builds on some of the longwall enabling technologies
CSIRO Mining Automation group
Main project stages
  Stage 1: Requirements Analysis – automation roadmap
  Stage 2: Navigation Sensor Development
  Stage 3: Open Communications and interoperability
Future proposed stages
  Stage 4; CM Navigation and Control System Development
  Stage 5: Mine-to-Plan Tool Development
  Stage 6: Field Trials
Notes: <number>

## Slide 4: CM/Shuttle Car/Cont Haulage Automation
Notes: <number>

## Slide 5: CM guidance
Haulage automation
Bolting automation
Data
Data
Notes: <number>

## Slide 6: Haulage automation
Notes: <number>

## Slide 7: Haulage automation
Notes: <number>

## Slide 8: Past mining guidance (inertial) R&D
Continuous Miner guidance
  Extensive INS testing conducted by USBM in 1990s
  Required accuracy could not be achieved
  Did not produce a practical solution
Highwall guidance
  INS first mounted on a CM (Addcar highwall) by CSIRO in 1998
  Guidance system was refined over a number of years
  Independent survey confirmed 8cm cross-track error at 384m
  Position error is distance (but not time) dependent
  Now a commercial product
Notes: <number>

## Slide 9
CM inertial position measurement
Field-proven for CM in highwall mining automation
Notes: <number>

## Slide 10: Past mining guidance (inertial) R&D
Longwall guidance
  INS first mounted on shearer by CSIRO in 2002
  Independent survey confirmed a 2-3cm 3D position accuracy
  Sustained performance (not time or distance dependent)
  Now a commercial product – LASC technology
Notes: <number>

## Slide 11
Longwall Shearer Inertial position measurement
Field-proven in longwall mining automation
Notes: <number>

## Slide 12: Inertial position measurement
High performance requires reliable odometry – potential sources
  Traction drive movement – too much slip
  Scanning lasers – proven technology but requires maintenance, could also provide some localisation, attitude and proximity information.
  Radar – some new emerging technologies, needs to be field-proven, could also provide additional information (including horizon control)
  ZUPTing?
INS
Scanning
lasers
Radar
Machine traction
Notes: <number>

## Slide 13: Scanning laser motion detection
Longwall laser-based creep/retreat measurement
Retreat direction (chainage)
Creep (gateroad alignment)
Notes: <number>

## Slide 14: Key deliverables of present project
CM automation roadmap
Demonstration of practical inertial navigation solution for CM guidance to provide accurate 3D position and attitude
Evaluation of localisation technology
Specifications for industry standard CM data interfaces to support CM automation, haulage, bolting, and mesh/support
Notes: <number>

## Slide 15: Key deliverables in future project
Demonstration of core navigation/control for automated and intelligent CM guidance and cycle management
Demonstration of integrated mine-to-plan system
Field demonstration of full system under practical controlled conditions
Notes: <number>

## Slide 16: Requirements for success
The successful project outcome will draw on
  Industry/OEM support – Vale CM and demo site
  Co-operation and co-ordination between CM2010 research groups
  Detailed CM automation roadmap
  Development of high performance inertial technology and navigation algorithms optimised for CM automation
  Development of suitable localisation technologies and algorithms
Notes: <number>

## Slide 17: Thank you
Contact Us
Phone: 1300 363 400 or +61 3 9545 2176
Email: enquiries@csiro.au Web: www.csiro.au
Exploration ad Mining
Dr David Hainsworth
Senior Principal Research Engineer
Phone: 07 3327 4420
Email: david.hainsworth@csiro.au
Exploration ad Mining
Dr David C. Reid
Principal Research Engineer
Phone: 07 3327 4437
Email: david.reid@csiro.au
Notes: <number>