## Slide 1
Nathan Thompson Assistant Mechanical Engineer
Conveyors – Management of Catastrophic Risk
Notes: At this time, Vic and I would be glad to take your questions.

## Slide 2: A Brief History of Metropolitan Colliery
Metropolitan Colliery is located about 1 hr drive south of Sydney in the southern coal fields, within the township of Helensburgh.
The mine opened in 1888
The mine is currently owned and operated by Peabody Energy
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 3: Slide title
Sub heading
Insert photo of Helensburgh without mine plan
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 4
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 5: What is a Catastrophic Risk in an Underground Coal Mine?
The events that are of a Catastrophic Risk involving an Underground Coal Mine Conveyor system are:
    Entanglement
    Fire

## Slide 6: Our Conveyor System
Belt | Conveyor Length | Belting Length | Width
MD1 | 553 m | 1115 m | 1050mm
MD2 | 627 m | 1265 m | 1050mm
T1 | 1360 m | 2735 m | 1050mm
T2 | 1300 m | 2620 m | 1050mm
T3 | 140 m | 290 m | 1050mm
T4 | 390 m | 790 m | 1200mm
T5 | 1300 m | 2620 m | 1200mm
T6 | 2600 m | 5240 m | 1200mm
V | 500 m | 1200 m | 1050mm
W | 1140 m | 2480 m | 1050mm
NWR | 1350 m | 2725 m | 1200mm
20M/G | 3360 m | 6900 m | 1050mm
21M/G | 200 m | 420 m | 1050mm
TOTAL | 14.820Km | 30.4Km | 
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 7: High Potential Incidents
WHEN | BELT | ROOT CAUSE
14/02/2002 | D3 | Burned out open motor
14/01/2004 | D2 | Failed bearing in drivehead
28/07/2004 | T5 | Collapsed idler at transition bootend
10/01/2005 | MD2 | Belt rubbing on concrete block
12/04/2007 | T6 | Belt tracked off at drivehead rubbing on side of drive. (servo roller in tracker fell down)
30/10/2007 | T4 | Collapsed idler at bootend heated
14/02/2008 | MD1 | Stone (spillage) jammed on bottom belt
21/05/2008 | T6 | Collapsed Head pulley
13/08/2008 | 20M/G | Belt tracked off at 1c/t and cut through stand.
31/12/2008 | T2 | Belt Tracked off at D/Head rubbed against side wall. Glowing embers. Start up after extended shutdown. Dry belt
17/3/2009 | MD2 | Belt rubbed on concrete blocks
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 8
Inspections
Belt attendants
Deputy Inspection
Design
Fit for purpose
equipment
Thermography
Vibration
analysis
Concrete
Close Inspection
CO Detection
Installation
RTD’s
Maintenance
TARP
Labour
Training
FRAS
Budget
Management plans
Where to go from there?

## Slide 9: Conveyor TARP
Sub heading
Bullet points
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 10
Inspections
Belt attendants
Deputy Inspection
Design
Fit for purpose
equipment
Thermography
Vibration
analysis
Concrete
Close Inspection
CO Detection
Installation
RTD’s
Maintenance
TARP
Labour
Training
FRAS
Budget
Management plans
Conveyor Crews
Where to go from there?

## Slide 11: Introduction of Belt Crews- 27th April 2009
There Mission
There Goal
To supply the mine with safe, efficient and reliable Conveyor system, capable of conveying sufficient product to meet the mine business plan. The conveyors will be maintained to a high standard by a skilled workforce.
12 months Conveyor High Potential Incident Free.
HOW?
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 12: The Belt Crews Dutie’s
Installations to a high standard
Inspections
    Statutory
    Audits
Belt Maintenance
    Mechanical
    Electrical
    Belt cleaning
Management of Defects new & old.
    Identify , resource & eliminate
Project work
Continual improvement
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 13: Conveyor Team Structure
Conveyor Engineer
Conveyor Leading Hand
Night Shift Conveyor Team
Dayshift Conveyor team
Belt Fitter
Belt Electrician
Belt Operator
Belt Fitter
Belt Electrician
Belt Operator
Belt Operator
Belt Operator
Belt Operator
Belt Operator
Belt Operator
Belt Operator
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 14: Success So Far?
No High Potential Incidents since the implementation of the conveyor crews, leading to our goal of No HPI’s
855 Defects found and rectified
1173 areas of spillage cleaned
Belt availability has increased
Production records have been broken

## Slide 15: Continuous Improvement
Conveyor workgroup
  Meet every 2 months
  Group consists of Engineers, Trades, Operators and Deputies
  Regular Audits
Designing of new equipment to improve efficiency
Root Cause Analyses to remove the issues not just fix them when they happen
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 16: The Future… How Does it Look?
Future upgrades
New lease area etc
Existing Office Buildings
Existing 600 tph conveyor
Existing Workshop
Notes: <number>
First… a bit about Peabody.
We are the world’s largest private-sector coal company in terms of tons sold and industry-leading reserve base. We have 125 years of mining expertise and offer world-class practices in safety, production and land restoration.
We are honored to be among Fortune’s Most Admired companies and have earned accolades for industry leadership at the Global Energy Awards and others.
Anyone questioning the concept of coal’s role in energy security need only look at the 25-meter-thick coal seam in this slide, at the largest and most productive mine in the world, where we mine 100 MTPA from a single mine… our North Antelope Rochelle Mine in the American West.

## Slide 17: The Future… How Does it Look?
New 3,500 tph conveyor
New Workshop
New Office Building

## Slide 18
Nathan Thompson Assistant Mechanical Engineer Thank you
Notes: At this time, Vic and I would be glad to take your questions.